## Slide 2: Computer Networking
Transmission media
By: Suresh Khanal
For http://mcqSets.com
Lesson #2

## Slide 3: Topics:
What is transmission media
Types of transmission media
  Bound transmission media
  Unbound transmission media

## Slide 4: What is transmission media

## Slide 5
Transmission media is the pathway through which data travels in a network. It can be guided as in cables or wires and also unguided transmission media such as in wireless transmission.

## Slide 6
Cables used to connect the different nodes of network are also called bound transmission media as they are bound by physical geography.

## Slide 7
Thus, for wireless connections, that are not bound by physical geography are called unbound transmission media

## Slide 8: Types of transmission media

## Slide 9: Types of transmission media
Bound transmission media or Guided transmission media
  Twisted Pair Cables
  Co-axial Cables
  Fibre Optics Cable
Unbound transmission media or Unguided transmission media
  Microwave
  Radiowave
  Infrared

## Slide 10: 1. Bound transmission media

## Slide 11: Bound Transmission media
The type of media that is bound by physical geography such as cables are known as bound transmission media. Twisted pair cables, Co-axial cables, Fibre optics cables etc. are the examples.

## Slide 12: 1.1 Twisted Pair Cables

## Slide 13: Twisted Pair Cables
A pair of wires twisted with each other. The conductor (copper) is cover with insulator and 4 pairs of such are packed inside cable jacket to make a network cable.

## Slide 14: Twisted Pair Cables

## Slide 15: Different category Twisted Pair Cables
https://www.linkedin.com/pulse/guide-choosing-suitable-ethernet-cables-kerry-zhang

## Slide 16: RJ45 for Twisted Pair Cables
https://www.linkedin.com/pulse/guide-choosing-suitable-ethernet-cables-kerry-zhang

## Slide 17: RJ45 Ports

## Slide 18: Types of transmission media
Bound transmission media or Guided transmission media
  Twisted Pair Cables
  Co-axial Cables
  Fibre Optics Cable
Unbound transmission media or Unguided transmission media
  Microwave
  Radiowave
  Infrared

## Slide 19: 1.2 Co-Axial Cables

## Slide 20: Co-Axial Cable
A solid central conductor surrounded by insulating material and then by a cylindrical shield woven from fine wires is known as co-axial cable.

## Slide 21: Co-Axial Cable
Co-axial cables are terminated with a connector known as BNC connector

## Slide 22: 1.3 Fiber-Optics cable

## Slide 23: Fiber-Optics cable
A cable with central glass tube covered with protective shield which transmit data using photons is fiber optics cable. These cables transmit data via concentrated bursts of laser beams which are carried through bundles of hair thin glass fibers.

## Slide 24: Fiber-Optics cable
A cable with central glass tube covered with protective shield which transmit data using photons is fiber optics cable. These cables transmit data via concentrated bursts of laser beams which are carried through bundles of hair thin glass fibers.

## Slide 25: Fiber-Optics cable
Physical look of fiber optic cable terminated with SC connector

## Slide 26: Fiber-Optics cable Connectors

## Slide 27: Types of transmission media
Bound transmission media or Guided transmission media
  Twisted Pair Cables
  Co-axial Cables
  Fibre Optics Cable
Unbound transmission media or Unguided transmission media
  Microwave
  Radiowave
  Infrared

## Slide 28: 2. Unbound Transmission Media

## Slide 29: Unbound Transmission Media
Unbound transmission media extend beyond the limiting confines of cabling.
They provide an excellent communication alternative for WANS. The lack of physical restrictions provides larger bandwidth as well as wide area capabilities. Unbound media typically operate at very high frequencies.
The three types of unbound transmission media are: Radio wave, Micro wave, Infrared

## Slide 30: Radio Wave
Radio waves makes it possible to connect to the network when running cables is difficult or more expensive.
In wireless networking, air is the vehicle through which the data is carried, just as Ethernet uses copper cable

## Slide 31: Radio Wave
Credits: https://www.slideshare.net/SameerFarooq2/sameer-farooq

## Slide 32: Microwave
Microwaves have been used in data communications for a long time. They have a higher frequency than radio waves and therefore can handle larger amounts of data.
Microwave transmission is line of sight (LOS) transmission. The transmit station must be in visible contact with the receive station. This sets a limit on the distance between stations depending on the local geography. Typically the line of sight, due to the Earth’s curvature, is only 50 km to the horizon! Repeater stations must be placed so the data signal can hop, skip and jump across the country.

## Slide 33: Infrared
Infrared offers a great unbound photonic solution. Like fiber-optic cabling, infrared communications use light, so they are not bound by the limitations of electricity.

## Slide 34
Thank You